###### Default Stress Orientation and Fault Geometry conventions in SeisSol 3D ( friction.f90)
From SeisSol 3D revision number 806 (Dec 4 2012) the following definitions regarding fault and stress orientation are convention. Matlab scripts ‘stressrotation2D’ and ‘stressrotation3D’ are available for a correct rotation of initial stress values on arbitrary orientated faults. Attention: Be aware that the 2D Version of SeisSol requires exactly opposed sign conventions.

###### Definitions

- Traction = normal vector n * stress tensor sxyz
- Normal stress = negative in compression
- Cohesion = negative, must be manually added to stress drop output
(acts on shear stress components, encapsulates the effect of pore pressurization)
Reference point = defines dip direction, starting point of the normal vector n pointing towards the fault, at +y
###### Fault geometry

Right-handed coordinate system required
        Please, make sure to follow this convention during model/mesh generation!

z y	free-surface North
        ↑ ↗	↑ ↗
↑ ↗	↑ ↗
↑ →→→ x	=	↑ →→→	East
        -z	depth

Arbitrary fault orientation possible, except a fault in the xy-plane, i.e. parallel to the free surface

Output in fault coordinate system
n = normal vector, from + y → - y
s = along-strike vector
d = along-dip vector, pointing in -z direction (downwards)

        nx	ny	-sy*nz
n = ( ny )	s = ( - nx ) * sqrt ( nx^2 + ny^2 )	d = (	sx*nz ) / || d ||
        nz	0	sy*nx - ny*sx

###### Examples

Attention: SCEC defines normal stress as positive in compression, opposite to SeisSol 3D convention.

SCEC TPV14 und TPV15 (branching fault geometry)

3D, right-lateral main fault in xz-plane (TPV14)
normal stress syy	= -120 MPa
shear stress sxy	= +70 MPa
nucleation patch shear stress	= +81.6 MPa

branch in -y direction (transformation by Theta= 330 degree )
normal stress sxx	= + 30.62.. MPa
normal stress syy	= - 150.62.. MPa
shear stress sxy	= - 16.96.. MPa

3D, left-lateral main fault in xz-plane (TPV15)
normal stress syy	= - 120 MPa
normal stress sxy	= - 78 MPa
nucleation patch shear stress	= - 81.6 MPa

branch in -y direction (transformation by Theta= 330 degree )
normal stress sxx	= - 97.55.. MPa
normal stress syy	= - 22.45.. MPa
shear stress sxy	= - 90.96.. MPa

SCEC TPV10 (dipping fault geometry)

3D, normal fault in xz-plane dipping 60 degree in -y-direction
Depth |-z| dependent initial stresses (syy= - 7378 Pa and syz = 4058 Pa at z=-1 m), rotation by theta=-30 degree

normal stress syy	= - 2019.26.. Pa * | -z |
normal stress szz	= - 5358.74.. Pa * | -z |
shear stress syz	= + 5223.72.. Pa * | -z |
cohesion	= - 0.2 MPa

Nucleation patch: add rotated cohesion of -0.2 MPa to increased initial stress values
shear stress=cohesion+(static friction cofficient + 0.0057)* initial normal stress

normal stress syy	= - 641.03.. Pa * | -z |
normal stress szz	= - 6736.97.. Pa * | -z |
shear stress syz	= + 6019.43.. Pa * | -z |

cohesion cyy	= - 173205 Pa
cohesion czz	= +173205 Pa
        cohesion cyz	= - 100000 Pa